## Slide 1: Parameter/State Estimation and Trajectory Planning of the Skysails flying kite system
Jesus Lago, Adrian Bürger, Florian Messerer, Michael Erhard Systems control and optimization laboratory- IMTEK University of Freiburg, Germany

## Slide 2: Overview
System Model
State estimation
  Importance of wind direction estimation
  Results
Parameter estimation
  Introduction to PECas
  Parameter estimation results
Planning of optimal trajectories

## Slide 3: Flying kite model dynamics
  Inputs:
    δ: steering deflection
    vwinch: winch speed
  Parameters
    E: glide ratio of the kite
    gk: proportional gain
    vw: wind speed at kite altitude
  State space:
    ϑ: angle tether-x axis (wind direction)
    φ: angle tether projected XZ plane and z axis
    ψ: angle roll axis and wind direction
    l: tether length
  Others:
    va: air path speed

## Slide 4: Kite model dynamics
  Motivation:
    Simplified dynamics
    Symmetric w.r.t wind direction (x-axis)
    Accurate for state prediction
    Fast for online estimation
    Probably suitable for NMPC

## Slide 5: State Estimation – Main Motivation
?
?
?
?
?
Wind importance in the model
  Model referenced respect to wind direction
  Wind speed included in the model
  Wind direction and speed measured at ground differs from flight altitude
   Some estimation needed

## Slide 6: State Estimation – Wind Speed Results
  Ground unit data useless for wind estimation at flight altitudes
  Current estimation: variability  power vs. retraction phase
  EKF based on model: better estimation with lower variability

## Slide 7: Introduction to PECas
Easy-to-apply parameter estimation software for application within the HIGHWIND project
Uses a direct collocation approach using IPOPT from CasADi
Provides possibilities for comfortable results interpretation
Main developer: Adrian Bürger (Still under development)
Tutorial, documentation and more: syscop.de/pecas

## Slide 8: Parameter Estimation
Motivation
  Change in parameters shows changes or problems in flying conditions
  Online estimation of parameters desired
Challenges
  Fast estimation for real time implementation
  Simplified dynamical model  not every assumption holds constantly
  Model sensitive to wind direction
  Unknown variance of measurement errors  weighting matrix problem

## Slide 9: Parameter Estimation – Main results
Setup of best trade off accuracy vs speed
  T = 0.4 s - f = 2.5 Hz
  5 minutes horizon – 40 minutes of data analyzed
  Collocation structure - 3rd order polynomial
  70 s. simulation time
  E = 4.1 ± 0.23
  gk = 0.087 ± 0.002
  R2 = 99 %

## Slide 10: Parameter Estimation – Trade off
Study of horizon length:
  σE and estimation time as critical parameter
  Trade off accuracy vs. speed: 5 minutes

## Slide 11: Parameter Estimation – Trade off
Study of sampling frequency:
  σE low variability, mostly estimation time critical
  Trade off accuracy vs. speed: 2.5 Hz

## Slide 12: Parameter Estimation – Trade off
Study of polynomial order:
  No influence on σE , almost no influence on estimation time

## Slide 13: Optimal trajectory planning
Experimental cycles
M. Erhard, H. Strauch, Flight control of tehered kites in autonomous pumping cycles for airborne wind energy, Control Engineering Practice (2015),
http://dx.doi.org/10.1016/j.conengprac.2015.03.001
 But, are they optimal?

## Slide 14: Optimal trajectory planning - Video
Video
Problem
Algorithm
  Casadi implementation
  Multiple shooting
  250 states

## Slide 15: Conclusion
Different ongoing work:
  State / Parameter estimation
  Trajectory Planning
Several obstacles / constrains:
  Computing speed
  Accuracy
Future plan
  Use current work to implement NMPC for trajectory control and test NMPC controller with real SkySails Power prototype

## Slide 16
Thank you for your attention. Questions/suggestions are welcome!